Function allmargin()
Sys = ALLMARGIN(SYS) provides detailed information about the gain, phase,
and delay margins and the corresponding crossover frequencies of the
SISO open-loop model SYS.

The output S is a structure with the following fields:
  * GMF: all -180 deg crossover frequencies in rad/TimeUnit
  * GM: corresponding gain margins (g.m. = 1/G where G is the
    gain at crossover)
  * PMF: all 0 dB crossover frequencies (in rad/TimeUnit)
  * PM: corresponding phase margins (in degrees)
  * DM, DMF: delay margins (in the units specified
    in SYS.TimeUnit for continuous-time systems, and in multiples of
    the sample time for discrete-time systems) and corresponding
    critical frequencies
  * Stable: 1 if stable, 0 if unstable, and NaN
    if stability cannot be assessed (as in the case of most FRD systems)

Sys = ALLMARGIN(MAG,PHASE,W,TS) computes the stability margins from the
frequency response data W, MAG, PHASE and the sampling time TS. ALLMARGIN
expects gain values MAG in absolute units and phase values PHASE in
degrees.

EXAMPLE :
sys = syslin('c',(s +8)/(s^3+7*s^2+8*s+6))
a = allmargin(sys1)

// References :
http://www.scilab.org/resources/documentation ;
http://spoken-tutorial.org/
http://in.mathworks.com/help/control/ ;
http://in.mathworks.com/help/control/ref/allmargin.html ;
https://en.wikipedia.org/wiki/Control_systems;

Author (s):
Sanchit Gupta & Ashutosh Kumar Bhargava