Function margin()
[Gm,Pm,Wcg,Wcp] = MARGIN(SYS) computes the gain margin Gm, the phase margin Pm, and the associated frequencies Wcg and Wcp, for the SISO open-loop model SYS (continuous or discrete). The gain margin Gm is defined as 1/G where G is the gain at the -180 phase crossing. The phase margin Pm is in degrees.

[Gm,Pm,Wcg,Wcp] = MARGIN(MAG,PHASE,W) derives the gain and phase margins from the Bode magnitude, phase, and frequency vectors MAG, PHASE, and W produced by BODE. MARGIN expects gain values MAG in absolute units and phase values PHASE in degrees.

MARGIN(SYS), by itself, plots the open-loop Bode plot with the gain and phase margins marked with a vertical line.

EXAMPLES
//Example 1:
s = %s ;
sys = syslin('c',3/(s^3+7*s^2+8*s+5)) ;
[GM,PM,Fgm,Fpm] = margin(sys) ;

//Example 2:
z = %z ;
sys1 = syslin('d',4/(z^2+7*z+8)) ;
margin(sys1) ; //Plots bode plot showing phase margin, gain margin etc
//Example 3:
sys1 = syslin('c',(s +8)/(s^3+7*s^2+8*s+6))
[Gm,Pm,Wcg,Wcp] = allmargin(sys1)

References :
http://www.scilab.org/resources/documentation ;
http://spoken-tutorial.org/
http://in.mathworks.com/help/control/ ;
http://in.mathworks.com/help/control/ref/margin.html ;
https://en.wikipedia.org/wiki/Control_systems;

Author (s):
Sanchit Gupta & Ashutosh Kumar Bhargava