function stepinfo(sys)
This function computes sytem characteristics when step input is given to the system.
stepinfo(Y,T,YFINAL) computes the following parameters assuming zero initial conditions and no input offset.
- RiseTime: rise time of the system
- SettlingTime: settling time
- SettlingMin: min value of Y once the response has risen
- SettlingMax: max value of Y once the response has risen
- Overshoot: percentage overshoot (relative to YFINAL)
- Undershoot: percentage undershoot
- Peak: peak absolute value of Y
- PeakTime: time at which peak absolute value is reached.

stepinfo(Y,T,YFINAL)
For SISO systems Y and T are vectors of same length NS.
For MIMO systems with NU inputs, NY outputs, Y should be
specified as an array of size NS-by-NY-by-NU.
Similarly, YFINAL should be specified as a NY-by-NU array.
Then the function returns an output array of each quantity
of size NY-by-NU.

stepinfo(Y,T) uses the last sampled value of Y as the YFINAL
stepinfo(Y) assumes T = 1:NS.

stepinfo(sys) calculates the time response characteristics of
dynamic system sys. The Rise Time, Settling Time etc. are all
calculated in Time Units of the system.

The default value of RiseTimeLims = [0.1 0.9] ie. from 10% to 90% of the final value.
The user may change the limits by setting RiseTimeLims to the desired values.
Example :
If the desired value of rise time is from 5% to 95% of the final value, then the command looks like
stepinfo(y,t,yfinal,'RiseTimeLims'[0.05 0.95])

Settling time with default 2% limits
The user may change this by setting SettlingTimeThreshold to the desired value.
Example :
If the desired value of settling time threshold is 5% of the final value, then the command looks like
stepinfo(sys,'SettlingTimeThreshold',0.05)

The function is also capable of giving Rise time high and rise time low. These values are not printed by default but they can be assigned to a variable.
RiseTimeHigh, RiseTimeLow can be extracted using the function in the following way
Example :
[x1 x2 x3 x4 x5 x6 x7 x8 x9 x10] = stepinfo(Y,T,YFINAL)
Then the variables x9 and x10 will give the values of RiseTimeHigh and RiseTimeLow respectively.

Example:
 s = %s ;
 sys = syslin('c',(s+6)/(s^2+6*s+4)) ;
 stepinfo(sys) ;

 References :
- http://www.scilab.org/resources/documentation ;
- http://spoken-tutorial.org/
- http://in.mathworks.com/help/control/ ;
- http://in.mathworks.com/help/control/ref/stepinfo.html ;
- https://en.wikipedia.org/wiki/Control_systems;

 Author(s):
 Sanchit Gupta